## Slide 1: Updates
Olivier Bergeron

## Slide 2: Since last time
Two main goals
  1- Keep searching for articles for correlation between electrode count and classification accuracy
    Didn’t find any more valuable article as of right now
  2- Find more articles about motor unit decomposition

## Slide 3: Motor Unit
Definition: A motor unit consist of a motor neuron and all the muscle fibers innervated by the axon.
Smallest functional unit of voluntary muscle activation
S. K. Gollapudi, J. J. Michael, and M. Chandra, Striated Muscle Dynamics, Reference Module in Biomedical Sciences. Elsevier, 2014. doi: 10.1016/B978-0-12-801238-3.00251-8.

## Slide 4: Motor unit vs EMG
D. Farina et A. Holobar, « Characterization of Human Motor Units From Surface EMG Decomposition », Proc. IEEE, vol. 104, no 2, p. 353‑373, févr. 2016, doi: 10.1109/JPROC.2015.2498665.

## Slide 5: Motor Unit Decomposition
Multiples techniques for extracting motor units spike trains
  Blind Source Separation
    Separates mixed signals into their original independent sources without prior knowledge of the mixing process.
  Convolution Kernel Compensation
    Reconstructs motor unit spike trains by compensating for the convolution effect of motor unit action potentials in EMG signals.
  Template matching + clustering
    Detects and classifies recurring signal patterns (spikes) by comparing them to learned templates and grouping similar ones into clusters.

## Slide 6: What information can be extracted
Firing rate of motor units
Recruitment order
Spike timing
Spatial location

## Slide 7: Pros with motor unit decomposition
Ability to find subtle gestures
  Some EMG patterns overlap for different motor unit activity
High quantity of recognisable gestures with high classification accuracy
  Example of quantity of gestures: 12 (94.6%)1, 66 (≥ 89%)2
High classification accuracy
  Around the same as CNN
[1] C. Chen, Y. Yu, X. Sheng, J. Meng, et X. Zhu, « Real-Time Hand Gesture Recognition by Decoding Motor Unit Discharges Across Multiple Motor Tasks From Surface Electromyography », IEEE Trans. Biomed. Eng., vol. 70, no 7, p. 2058‑2068, juill. 2023, doi: 10.1109/TBME.2023.3234642.
[2] M. Montazerin, E. Rahimian, F. Naderkhani, S. F. Atashzar, S. Yanushkevich, et A. Mohammadi, « Transformer-based hand gesture recognition from instantaneous to fused neural decomposition of high-density EMG signals », Sci Rep, vol. 13, no 1, p. 11000, juill. 2023, doi: 10.1038/s41598-023-36490-w.

## Slide 8: Cons with motor unit decomposition
Highly sensitive to electrode shift
  Often required to re-decompose the motor units when shifting happens
More “hardware hungry”
  Decompositions methods are more computationally intensive
  More power is needed
  Very difficult for real-time application
Highly sensitive to positioning
  Misalignments/changes in contact degrades motor unit tracking quality
  When redonned, recalibration is required

## Slide 9: What if: hybrid method
Hybrid method: Combine motor unit decomposition with CNN features
Why?
  Robustness, fast computing and general hand gestures with CNN
  Fine neural control details with motor unit decomposition

## Slide 10: What if: hybrid method
Methods examples
  Early fusion: Concatenate EMG + Motor Unit into one input
  Late fusion: Two separate classifier fused at decision level
  Joint fusion: Models with dual-branches and adaptive weighting
Applications
  High gesture count applications
  Benchmarking upper limits of classification performance

## Slide 11: Pros and Cons
Pros
  Combining increase accuracy
  More gesture recognition
  Can give neural control information
Cons
  High computing cost
  Very hard for wearable devices
  High sensibility with steep performance reduction risk