## Slide 1: Avancements
Olivier Bergeron

## Slide 2: Since last time
Project finally got defined
  Design a HD-EMG forearm sleeve with high count of electrodes (≥ 256 channels) aimed at detecting and decomposing motor unit activity to enable accurate hand movement recreation in an offline environment.
  Definition still w.i.p.
Start defining project needs/goals
  Multiple categories
    Mechanical
    Electronics
    Firmware
    Software

## Slide 3: Mechanical Design
First major design phase
Sleeve design
  Structure (Material, Shape, Size)
  Electrode design (Material, Size, Positioning, Quantity)
  Cable management
  Ease of use
Design approach: Custom

## Slide 4: Electronic Design
Second major design phase
Data acquisition design
  Acquisition module (Data to be read by an FPGA)
  FPGA module for acquisition
  GPU module for software use
Design approach: Not fully defined, but might go with overkill already existing design (try to avoid having it as a bottleneck)

## Slide 5: Firmware Design
Third major design phase
Data acquisition code
  Program the FPGA to get all the channels and transfer the data to a GPU
  Sampling frequency objective: 2 kHz

## Slide 6: Software Design
Last major design phase
Algorithm implementation
  Use of motor unit decomposition algorithms to reconstruct hand movements

## Slide 7: Some start of mechanical design
Context: Electrodes needs to be small and close to each other for motor unit decomposition
Rule of thumb: IED ≈ 2 x Electrode diameter
  With a small electrode diameter
    More motor units will be detectable
    Noisier the signal will be
    Sweet spot seems to be between 2 mm and 4 mm

## Slide 8: Some start of mechanical design
Example
  265 mm circumference where the sleeve will be
  With an IED of 4 mm => approx. 67 electrodes needed for 1 row of electrodes
  If we want 256 electrodes max => only 3 columns are possible
Three possible approaches:
  1- More electrodes
  2- Increase IED (Higher and/or asymmetrical values)
  3- Half sleeve instead of full sleeve

## Slide 9: Some start of mechanical design
What have been found so far
  Avoid half sleeve because of less detectable motor units
  Asymmetrical IED values, since circumferential coverage is more important than longitudinal coverage
  To keep electrodes small and close, higher electrode count will be needed
First draft: 60 x 8 grid with circumferential IED close to 4 mm and longitudinal IED of 10 mm

## Slide 10: Next steps
Figure out if there is a maximum of channels electronic wise
Try different grid values
Simulate coverage when forearm size change