## Slide 1: Update
Olivier Bergeron

## Slide 2: PEDOT article no 1
Conducting Polymer-Ionic Liquid Electrode Arrays for High-Density Surface Electromyography (Velasco-Bosom et al.)
Key points
  Grid size: 4 x 4
  Electrode size: 1.5 mm x 1.5 mm
  IED: 3 mm
  Scalable fabrication techniques

## Slide 3: PEDOT article no 2
Stretchable and Self-Adhesive PEDOT:PSS Blend with High Sweat Tolerance as Conformal Biopotential Dry Electrodes (Cao et al.)
Key points
  Blend of PEDOT, Polyvinyl alcohol and tannic acid
  Lower peak noise than Ag/AgCl (20 µV vs 60 µV)
  Stretchable with minimal resistance change (up to 50% stretch)
  Self-adhesive on dry and sweaty skin

## Slide 4: Pre-made kits - TMSi
Electrode grid
  4 mm IED
  2 mm diameter (not written but assumed)
  32 and 64 channels available
  Textile grids
Wireless acquisition module
Free software
  Motor unit decomposition

## Slide 5: Pre-made kits - Ot Bioelettronica
Electrode Grid
  5 mm IED
  2.5 mm diameter (not written but assumed)
  32 channels available
Acquisition module
  High channel count available (384 or 960)

## Slide 6: Pre-made kits - Delsys
Electrode grid
  2 mm diameter
  6 mm IED
  Hard to generate bigger grid
Paid software
  API available
  Motor Unit Decomposition

## Slide 7: Explorable solution
Main issue: acquisition modules very expensive
  Possible solution: Custom made acquisition system
    Could be tested with commercial grid