## Slide 1: Presentation & Updates
Olivier Bergeron

## Slide 2: Project Presentation
EMaGer: Spatial EMG activation maps with 64 electrodes
F. Chamberland et al., « EMaGer: A Wearable Full-Circumference HD-EMG Sensor and Data Augmentation Method for Robust Hand Gesture Recognition », in 2023 45th Annual International Conference of the IEEE Engineering in Medicine & Biology Society (EMBC), Sydney, Australia: IEEE, juill. 2023, p. 1‑5. doi: 10.1109/EMBC40787.2023.10340612.

## Slide 3: Project Presentation
Hypothesis: More channels would result more recognisable gestures.
A. H. Caillet et al., « Larger and Denser: An Optimal Design for Surface Grids of EMG Electrodes to Identify Greater and More Representative Samples of Motor Units », eNeuro, vol. 10, no 9, p. ENEURO.0064-23.2023, sept. 2023, doi: 10.1523/ENEURO.0064-23.2023.

## Slide 4: Project Presentation
Electrode Grid
Analog Front End (AFE)
Analog to Digital Converter (ADC)
FPGA
Post-processing
(MUAP Decomposition)

## Slide 5: Project Presentation
Electrode grid: Custom made
  Grid size: 7 x 51 (357 total)
  Electrode dimensions: 2.5 mm
  Inter-electrode distance (IED): 5 mm (Circ.) and 10 mm (Long.)
AFE & ADC:
  High number of channels (448 or 512)
  Hardware options: Pre-made (TMSi, OT Bioelettronica, etc.), custom with INTAN or fully custom.
Post-processing
  Hardware not fully defined but gravitate towards GPU.

## Slide 6: Updates
PEDOT process:
  Found interesting articles.
  Will send them to Ricardo to review.
Prototype quotes:
  TMSi: Want to set up a meeting to discuss.
  OT Bioelettronica: Affordable grid, but not the acquisition module

## Slide 7: Updates