## Slide 1: Updates
Olivier Bergeron

## Slide 2: Electrode fabrication process
Answer from Ankur: Feasible

## Slide 3: Interesting articles (#1)
M. Chen et P. Zhou, « 2CFastICA: A Novel Method for High Density Surface EMG Decomposition Based on Kernel Constrained FastICA and Correlation Constrained FastICA », IEEE Trans. Neural Syst. Rehabil. Eng., vol. 32, p. 2177‑2186, 2024

## Slide 4: Interesting articles (#1)
2CFastICA: Upgrade from FastICA
  Open-source code available
Problems withs FastICA:
  Cannot differentiate a new motor unit from a time delayed equivalent of the first motor unit –> local convergence

## Slide 5: Interesting articles (#1)
First solution proposed: Progressive FastICA Peel-Off (PFP)
  To avoid rediscovering again the same motor unit, its contribution to the EMG signal is subtracted from the original signal. FastICA is then applied to the residual to find other motor units
  Problem with PFP:
    Needs accurate MUAP estimation
    Accumulation of errors
    Computationally expensive

## Slide 6: Interesting articles (#1)
New solution: 2CFastICA
  Instead of removing motor unit from the signal, it’s removed from the FastICA’s search space.
  Done mathematically through constraints instead of substraction

## Slide 7: Interesting articles (#1)
Experiments done:
  Simulation study
    Robust to noise
    Comparable to PFP
  Two-source validation (intramuscular EMG)
    Matching rate of 97%
  Two-source validation (ALS surface EMG)
    Matching rate of 99%

## Slide 8: Interesting articles (#1)
Advantages for 2CFastICA vs PFP:
  Faster
  More scalable
  Better suited for real-time applications

## Slide 9: Interesting articles (#2)
A. Ch. Lazanas et M. I. Prodromidis, « Electrochemical Impedance Spectroscopy─A Tutorial », ACS Meas. Sci. Au, vol. 3, no 3, p. 162‑193, juin 2023[1]
Method for measuring electrode impedance: Electrochemical impedance spectroscopy (EIS)
Reading in progess

## Slide 10: Interesting articles (#2)