## Slide 1: Update
2026-06-26

## Slide 2: FPGA
Code is working:
  Connect to the FPGA
  Detects if one Intan module is connected
  Read data and store it in PC
  Can easily do iteration when time comes
Small issue:
  Chip is running hot
  Will add a heatsink

## Slide 3: Breakout Board
Board is done
Just need to generate gerber files and order

## Slide 4: Electrode patch
Electrode shape
  13 microneedle / electrode
  5 mm spacing
  4 x 8 grid / patch
  50 µm diameter
  500 µm pitch
  400 µm length

## Slide 5: Electrode patch
General look of one patch
  Half like this, half “mirrored”
Work in progess
  Main focus
Electrode grid
Contact
With
Intan

## Slide 6: Intan module modification
I have the files from David-Alexandre
Will work on that after electrode sample

## Slide 7: To DO list
Order Breakout board
Finish first version of electrode patch for review
If I have the time, work on the Intan module modification